| Colour | Product Code | Pack Size | Box Qty |
| --- | --- | --- | --- |
| Grey | 145GY | C3 | 25 |

Product Description

145 Butyl Sealant is a traditional permanently plastic one component sealant based on Polybutene that provides an effective weatherproof seal in a variety of exterior and interior applications. 145 Butyl Sealant forms a skin in approximately 24hrs but remains permanently plastic underneath. The sealant accommodates joint movement of +/- 5%, is over paintable and exhibits good UV and chemical resistance.

Benefits

- Overpaintable.

- Adheres to most common building surfaces.

- Semi drying – forms a surface skin but remains permanently elastic beneath.

- High solids formulation - excellent gap filling properties without shrinkage.

- Good external weathering properties.

Areas For Use

- Single glazing of metal, concrete and wooden frames.

- Sealing metal roof panels.

- Pointing around soft and hardwood timber, metal and concrete/stone window and door frames.

- Sealing metal panels in car bodies and containers.

- Sealing pre-cast concrete panels.

- Sealing timber sections to brick, stone and concrete; ideal for rooflines applications.

- Sealing gaps and cracks in brickwork and stone.

Limitations

- Do not use in conjunction with bitumen or asphalt – use WEATHER MATE sealant.

- Do not use on plastic, PVCu windows, polycarbonate or acrylic sheet.

- The sealant will skin in 24-48 hrs but will remain plastic underneath.  For this reason, it should not be used in areas where it will be subjected to interference or damage (e.g. floor joints).  In these cases, use Polyurethane 40 Sealant.

- Do not use in applications where joint movement will exceed +/- 5%.

- It is the user’s responsibility to determine suitability for use.  If in doubt, please contact Technical Services department for advice.

Surface Preparation

All surfaces to be sealed must be sound, dry and clean.  The depth of the joint should be approximately 50% of the width.  Reduce joint depth with Fix & Fill Expanding Foam or Backer Rod.

Application

Cut the tip of the cartridge, taking care not to damage the thread.

Apply nozzle and cut cleanly at an angle of 45 degrees with an opening slightly larger than the gap to be sealed.

Apply using a standard sealant gun.  Best results will be obtained by keeping an even pressure on the gun trigger and keeping the gun at a constant angle to the surface to be sealed.

To ensure a proper bond, always smooth down sealant using a spatula or piece of wood wetted with soap and water solution.

Tool down within 1 hour of application.

Specific Data

| Form | Thixotropic paste (ready to use) |
| --- | --- |
| Application Temp | 5oC to 35oC |
| Coverage | Approx 11 linear meters per cartridge using a 6mm bead |
| Viscosity | 150-350,000cps |
| Cure | Skins within 24hrs remains elastic underneath. |
| Specific Gravity | 1.5-1.6 approx |
| Cleaner | White spirits. |
| Movement Accom | +/- 5% |
| Overpaintability | Most decorative paints. Compatibility test is always recommended. |

Health & Safety

Consult MSDS for full list of hazards

Storage

Store in original unopened containers between 15 and 20oC

Shelf Life

12 months from date of manufacture when stored in original unopened containers

The technical data contained herein is based on our present knowledge and experience and we cannot be held liable for any errors, inaccuracies, omissions or editorial failings that result from technological changes or research between the date of issue of this document and the date the product is acquired. Before using the product, the user should carry out any necessary tests in order to ensure that the product is suitable for the intended application. Moreover, all users should contact the seller or the manufacturer of the product for additional technical information concerning its use if they think that the information in their possession needs to be clarified in any way, whether for normal use or a specific application of our product. Our guarantee applies within the context of the statutory regulations and provisions in force, current professional standards and in accordance with the stipulations set out in our general sales conditions. The information detailed in the present technical data sheet is given by way of indication and is not exhaustive. The same applies to any information provided verbally by telephone to any prospective or existing customer.

# Text boxes

EVERFLEX 145 BUTYL SEALANT